|  | Nordisk Sikkerhet AS |
| --- | --- |
|  | Ref.: Personal protection equipment |
|  | Project title: “RN Material Detection, Protection, and Dosimetry Equipment for Mukachyvskyi Border Detachment, SBGS” |

Specifications

Supply of personal protection equipment

Contracting Authority: Nordisk Sikkerhet AS

Recipient: Mukachyvskyi Border Detachment of SBGS

Tenderer’s name: __________________________________

Contents

1.	PROTECTIVE SUITS	3

2.	PROTECTIVE GAS MASKS	5

3.	DELIVERY TERMS AND CONDITIONS	6

4.	WARRANTY AND POST-WARRANTY SERVICES	6

5.	TIME SCHEDULE	7

NOTE

The Tenderer shall fill in the Annex “Specifications” in the format given below.  The Tenderer’s proposed supplies should be manufactured and certified in accordance with the technical regulations and standards of Ukraine. The complete table should be submitted to the Contracting Authority along with the required tender documents. On the front page of the Annex “Specifications”, the Tenderer shall indicate its name. After the completion of this document, it should be signed and dated by the Tenderer-authorized person.

# PROTECTIVE SUITS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Manufacturer | — |  |
| Model | — |  |
| Scope of supply, including: | 44 sets |  |
| Number of suits |  |  |
| XXL size | 8 sets |  |
| L size | 14 sets |  |
| XL size | 22 sets |  |
| TECHNICAL SPECIFICATIONS |
| Type/design | Insulating protective suit for emergency team: Coverall with front zipper covered by double storm flaps which can be sealed by the wearer, hood with elastic face opening for tight fit around respirator, fit with protective gloves and boots |  |
| Radiation protection | Protection against surface radiation contamination (radioactive particles) |  |
| Category | Category III as per EU standard. Chemical protection clothing |  |
| Material | TYCHEM F |  |
| Material of boots | Butyl rubber, double coating |  |
| Material of gloves | Butyl rubber |  |
| Protection against radioactive particles | EN 1073-2:2002(1) |  |
| Protection against liquids under pressure of 3 Bar | Type 3B - EN 14605:2005 (DSTU EN 14605:2007) |  |
| Protection against liquid aerosols | Type 4 - EN 14605:2005 (DSTU EN 14605:2007) |  |
| Protection against airborne solid particles | Type 5 - EN ISO 13982-1:2004 (DSTU EN ISO 13982-1:2009) |  |
| Protection against liquid chemicals | Type 6 - EN 13034:2005 (DSTU EN 13034:2007) |  |
| Biological barrier | EN 14126:2003 (DSTU EN 14126:2008) |  |
| Period of validity, no less than | 4 years |  |
| PRESERVATION AND PACKAGING |
| Packaging | Protection for transportation, handling and reliable storage without re-preservation within 1 year upon delivery. |  |
| OTHER REQUIREMENTS |
| Certified for use in Ukraine | Yes |  |
| Visibility of Norwegian financing | Any equipment delivered under the contract should be clearly identified and the packaging should have indelible labels containing the flag of Norway and the phrase “Provided with support from the Government of Norway” in Ukrainian and in English. |  |
| DOCUMENTATION |
| User’s manual | in Ukrainian |  |
| Certificate of conformity or equivalent document attesting certification of PPE in Ukraine | in Ukrainian |  |
| Transportation documentation | in English and Ukrainian |  |

# PROTECTIVE GAS MASKS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Manufacturer | — |  |
| Model | — |  |
| Scope of supply, including: | 44 sets |  |
| Number of gas masks |  |  |
| S size | 8 sets |  |
| M size | 14 sets |  |
| L size | 22 sets |  |
| TECHNICAL SPECIFICATIONS |
| Type | Mask with a filter |  |
| Radiation protection | Protection against airborne radioactivity |  |
| Protection grade | 2-3 Class as per standard DSTU EN 136 (ДСТУ EN 136 in Cyrillic) |  |
| Material of gas mask | Halobutyl or EPDM (ethylene propylene diene monomer) |  |
| Filter | Resistance to air stream of 130 Pa or greater, Threaded joint diameter of 40 mm. |  |
| Type of protection | Chemical, radioactive and biological agents |  |
| Components | Gas mask, Filtering and absorbing element, Bag, Spare parts, tools and accessories (SPTA) |  |
| Front | Protection against chemical, radioactive and biological agents for 24 hours or greater, Resistance to respiration of no more than 250 Pa, Legibility of speech of 95% or greater |  |
| Weight, kg | ≤ 0.5 |  |
| Period of validity, no less than | 10 years |  |
| PRESERVATION AND PACKAGING |
| Packaging | Protection for transportation, handling and reliable storage without re-preservation within 1 year upon delivery. |  |
| OTHER REQUIREMENTS |
| Certified for use in Ukraine | Yes, certified for compliance with standard standard DSTU EN 136 (ДСТУ EN 136 in Cyrillic) |  |
| Visibility of Norwegian financing | Any equipment delivered under the contract should be clearly identified and the packaging should have indelible labels containing the flag of Norway and the phrase “Provided with support from the Government of Norway” in Ukrainian and in English. |  |
| DOCUMENTATION |
| User’s manual | in Ukrainian |  |
| Certificate of conformity or equivalent documentation attesting certification of PPE in Ukraine | in Ukrainian |  |
| Transportation documentation | in English and Ukrainian |  |

# DELIVERY TERMS AND CONDITIONS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DELIVERY TERMS AND CONDITIONS |
| Terms of Delivery | DDP, Incoterms 2010 |  |
| Place of Delivery | Mukachevo, Ukraine |  |
| Delivery Time | ≤ 90 calendar days after the date of contract signature |  |

# WARRANTY AND POST-WARRANTY SERVICES

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| WARRANTY AND POST-WARRANTY SERVICES |
| Duration of warranty period | ( 24 months |  |
| Place of warranty repairs and maintenance | Ukraine |  |
| Presence of official representative of the manufacturer or authorised service centre in Ukraine | Yes |  |
| Technical support during warranty and post-warranty period | Technical support by email or telephone in Ukrainian/English to solve any technical problems |  |
| After-sales service | Compulsory after-sales service to be provided under a separate agreement with the Recipient shall include the following: - Maintenance, if required, and post warranty repair of the Equipment on the territory of Ukraine; - Rapid provision of spare parts and consumables. |  |

# TIME SCHEDULE

| No. | Action | Period of completion | Tenderer’s Offer |
| --- | --- | --- | --- |
| Personal protection equipment |
| 1. | Submission of documents: User’s manual, Certificate of conformity or equivalent document attesting certification of equipment in Ukraine, Transportation documentation. | 2 weeks before the scheduled shipment and supplied with equipment |  |
| 3. | Equipment delivery | Within 90 calendar days after the signing of Contract |  |

Authorized person on behalf of the Tenderer:

Name: ____________________________________________

Title: ______________________________________________

Signature: ________________________________________

Date: ______________________________________________