|  | Nordisk Sikkerhet AS |
| --- | --- |
|  | Tender title: Supply of Isotope identification devices |
|  | Project title: “RN material detection, protection, dosimetry equipment and training for Zhytomyrskyi Border Detachment, SBGS, Ukraine” |

Specifications

Supply of isotope identification devices                                  (gamma spectrometers)

Contracting Authority: Nordisk Sikkerhet AS

Recipient: Zhytomyrskiy Border Detachment of SBGS

Tenderer’s name: __________________________________

Contents

1.	ISOTOPE IDENTFIFICATION DEVICE	2

2.	DOCUMENTATION	4

3.	DELIVERY TERMS AND CONDITIONS	4

4.	TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR	4

5.	WARRANTY AND POST-WARRANTY SERVICES	5

6.	TIME SCHEDULE	6

NOTE

The Tenderer shall fill in the Annex “Specifications” in the format given below.  The Tenderer’s proposed supplies should be manufactured and certified in accordance with the technical regulations and standards of Ukraine. The complete table should be submitted to the Contracting Authority along with the required tender documents. On the front page of the Annex “Specifications”, the Tenderer shall indicate its name. After the completion of this document, it should be signed and dated by the Tenderer-authorized person.

# ISOTOPE IDENTFIFICATION DEVICE

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Manufacturer | — |  |
| Model | — |  |
| Scope of supply | 1. Isotope identification device - 5 pcs. 2. Calibration/reference sources for routine operation (in case if there is no built-in reference source) – 5 pcs. |  |
| TECHNICAL SPECIFICATIONS |
| Type | Handheld device |  |
| Ionizing radiation | Gamma |  |
| Detector type | Spectrometric scintillation detector |  |
| Energy range of detected gamma radiation | From 50 keV to 3 MeV or better |  |
| Relative energy resolution for line of 662 keV (137Cs), no less than | 8 % |  |
| Automatic identification of radionuclides | - Nuclear materials: 233U, 235U, 239Pu; - Medical radionuclides: 18F, 67Ga, 99mTc, 111In, 123I, 125I, 131I, 133Xe, 192Ir, 201Tl; - Naturally occurring radioactive materials: 40K, 226Ra, 232Th, 238U; - Industrial radionuclides: 57Co, 60Co, 133Ba, 137Cs, 192Ir, 226Ra, 241Am. |  |
| Measurement of individual dose equivalent rate Hp(10) | From 0.01 μSv/h to 0.5 mSv/h or better |  |
| Channels of amplitude gamma spectrum, no less than | 1024 |  |
| Built-in radiation source for automatic calibration | Not required, but advantageous to have |  |
| Recording gamma spectra in a non-volatile memory | Yes |  |
| Functions | - Automated identification of gamma-emitting radionuclides; - Measurement of individual dose equivalent rate; - Indication of measured values on the built-in display; - Storing spectra in a non-volatile memory and transferring to the PC; - Radiation safety alarm; - Assistance to energy calibration of the spectrometer (would be an advantage). |  |
| Power supply | From integrated accumulators |  |
| Time of continuous operation at gamma background (not more than 0.5μSv/h) under non-alarm conditions, no less than | 8 hours |  |
| Total weight of all the components, no more than | 3.5 kg |  |
| Physical dimensions | Compact, portable, suitable for hand-held use |  |
| Waterproof, no less than | IP54 |  |
| Mean time between failures, no more than | 4000 hours |  |
| Service life, no less than | 6 years |  |
| ENVIRONMENTAL REQUIREMENTS |
| Ambient temperatures | From -20 to+45 0C |  |
| Relative humidity | Up to 95% at ambient temperature of 350C and lower, without condensation of moisture |  |
| PRESERVATION AND PACKAGING |
| Packaging | Protection for transportation, handling and reliable storage without re-preservation within 1 year upon delivery. |  |
| OTHER REQUIREMENTS |
| Certified for use in Ukraine | Yes |  |
| Visibility of Norwegian financing | Any equipment delivered under the contract should be clearly identified and should have metallic plates or indelible labels containing the flag of Norway and the phrase “Provided with support from the Government of Norway” in Ukrainian and in English. |  |

# DOCUMENTATION

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DOCUMENTATION |
| Technical specifications | In Ukrainian/Russian |  |
| Operator’s manual | In Ukrainian/Russian |  |
| Passports for technical means | In Ukrainian/Russian |  |
| Certificate of primary metrological verification | In Ukrainian/Russian |  |
| Pattern approval certificate or equivalent document attesting certification of measurement instrument in Ukraine | In Ukrainian/Russian |  |
| Training documentation | In Ukrainian/Russian |  |
| Transportation documentation | In English and Ukrainian |  |

# DELIVERY TERMS AND CONDITIONS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DELIVERY TERMS AND CONDITIONS |
| Terms of Delivery | DDP, Incoterms 2010 |  |
| Place of Delivery | 125 S. Paradzhanova St., 10025, Zhytomyr, Ukraine |  |
| Delivery Time | ≤ 90 calendar days after the date of contract signature |  |

# TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Place of training (training room to be provided by the Recipient) | Zhytomyrskiy Border Detachment of SBGS: 55A T. Shevchenko St., Ovruch City, 11101, Zhytomyr region, Ukraine |  |
| Duration of training course | 2 days |  |
| Language of training course | Ukrainian or English |  |
| Number of trainees, up to | 50 persons |  |
| Themes to be covered | - Nature of ionizing radiation, - Fundamentals of gamma-ray spectrometry, - Radioactive sources and nuclear materials to be detected using the isotope identification device, - Operating principles of measuring instruments, - Detailed analysis of algorithms and features of operation, - Use of measuring instrument, - Setting-up procedures, - Procedures of calibration and measurements, - Maintenance, - Minor repairs, - Specialized software: installation and operation. |  |
| Theoretical part duration, no less than | 1 day |  |
| Practical part duration, no less than | 1 day: practical training at Recipient’s training room and/or at border check point |  |
| Instructional video | Optional |  |
| Verification | Test, written form |  |
| TRAINING COURSE DOCUMENTATION |
| One certificate per trainee | In Ukrainian and English |  |
| List of materials to provide per trainee | - Set of training materials; - User’s documentation; - Training materials on one CD/DVD. |  |
| Training materials language | In Ukrainian/Russian |  |
| Results of test after training should be delivered to the Contracting Authority and Recipient | Yes |  |

# WARRANTY AND POST-WARRANTY SERVICES

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| WARRANTY AND POST-WARRANTY SERVICES |
| Duration of warranty period | ( 24 months |  |
| Place of warranty repairs and maintenance | Ukraine |  |
| Presence of official representative of the manufacturer or authorised service centre in Ukraine | Yes |  |
| Technical support during warranty and post-warranty period | Technical support by email or telephone in Ukrainian/English to solve any technical problems (software failure, anomalous behaviour, minor improvements concerning process, functional capabilities of data processing, etc.) and rectify any system-disabled state |  |
| After-sales service | Compulsory after-sales service to be provided under a separate agreement with the Recipient shall include the following: - Maintenance and post warranty repair of the Equipment on the territory of Ukraine; - Rapid provision of spare parts and consumables. |  |

# TIME SCHEDULE

| No. | Action | Period of completion | Tenderer’s Offer |
| --- | --- | --- | --- |
| 1. | Submission of documents: Technical specifications. | Within 45 calendar days after the signing of Contract |  |
| 2.. | Submission of documents: Operator’s manual, Passports/logbooks for technical means, Certificate of primary metrological verification, Pattern approval certificate or equivalent document attesting certification of measurement instrument in Ukraine Transportation documentation. | 2 weeks before the scheduled shipment and supplied with equipment |  |
| 3. | Submission of documents: Training course documentation. | 2 weeks before the scheduled training |  |
| 4. | Equipment delivery | Within 90 calendar days after the signing of Contract |  |
| 5. | Training of personnel | Within 90* calendar days after the signing of Contract |  |

Note: *) The personnel training must be carried out not later than within ninety (90) calendar days after the signing of Contract. The actual dates of training shall be confirmed by the Recipient and Contracting Authority no later than ten (10) days before the training course.

Authorized person on behalf of the Tenderer:

Name: ____________________________________________

Title: ______________________________________________

Signature: ________________________________________

Date: ______________________________________________