|  | Nordisk Sikkerhet AS |
| --- | --- |
|  | Tender title: Multifunctional survey meters for the detection of RN materials |
|  | Project title: “RN material detection, protection, dosimetry equipment and training for Zhytomyrskyi Border Detachment, SBGS, Ukraine” |

Specifications

Supply of multifunctional survey meters for

the detection of radioactive and nuclear materials

(dosimeter-radiometer)

Contracting Authority: Nordisk Sikkerhet AS

Recipient: Zhytomyrskiy Border Detachment of SBGS

Tenderer’s name: __________________________________

Contents

1.	MULTIFUNCTIONAL SURVEY METER FOR THE DETECTION OF RN MATERIALS	2

2.	DOCUMENTATION	5

3.	DELIVERY TERMS AND CONDITIONS	5

4.	TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR	5

5.	WARRANTY AND POST-WARRANTY SERVICES	6

6.	TIME SCHEDULE	7

NOTE

The Tenderer shall fill in the Annex “Specifications” in the format given below. The Tenderer’s proposed supplies should be manufactured and certified in accordance with the technical regulations and standards of Ukraine. The complete table should be submitted to the Contracting Authority along with the required tender documents. On the front page of the Annex “Specifications”, the Tenderer shall indicate its name. After the completion of this document, it should be signed and dated by the Tenderer-authorized person.

# MULTIFUNCTIONAL SURVEY METER FOR THE DETECTION OF RADIOACTIVE AND NUCLEAR MATERIALS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Manufacturer | — |  |
| Model | — |  |
| Scope of supply | 10 pcs |  |
| TECHNICAL SPECIFICATIONS |
| Type | Handheld device |  |
| Detection channels | Alpha, Beta, Gamma |  |
| Detectors | Replaceable detectors attached to the carrying handle/telescopic arm |  |
| Functions | Search, localization and evaluation of RN materials: - Measurement of ambient dose equivalent and ambient dose equivalent rate H*(10) (alternatively, personal dose equivalent and personal dose equivalent rate Hp(10)); - Measurement of flux density and surface activity of alpha and beta emitters; - Natural and intrinsic background suppression; - Indication of measured values on the LCD display; - Audible signalling of each registered particle in the search mode; - Audible and visual alarm when thresholds are exceeded; - Adjustable thresholds for alarm; - Recording the measurements in the non-volatile memory. |  |
| Equipment | The survey meter shall be equipped with the following: set of radiation detectors, data display and processing unit, telescopic arm (of 1.2 m long or more), rechargeable battery, battery charger, set of cables, carrying case. |  |
| GAMMA MEASUREMENTS |
| Energy range of detected gamma radiation | From 60 keV to 3 MeV or better |  |
| Measurement range of ambient dose equivalent H*(10) (alternatively, personal dose equivalent Hp(10)) | From 0.1 μSv to 10 Sv or better |  |
| Measurement range of ambient dose equivalent rate H*(10) (alternatively, personal dose equivalent rate Hp(10)) | From 0.1 μSv/h to 2 Sv/h or better |  |
| Uncertainty of measuring ambient dose equivalent rate H*(10) when calibrated for 137Cs, no more than | ± 35% |  |
| ALPHA MEASUREMENTS |
| Energy range of detected alpha radiation | From 4 MeV to 7 MeV or better |  |
| Measurement range of alpha flux density | From 10 to 1(105 part./(cm2min) or better |  |
| Relative measurement error, no more than | ±20% |  |
| BETA MEASUREMENTS |
| Energy range of detected beta radiation | From 155 keV to 3 MeV or better |  |
| Measurement range of beta flux density | From 10 to 1(105 part./(cm2min) or better |  |
| Relative measurement error, no more than | ±20% |  |
| PERFORMANCE |
| Setup time of operating mode, no more than | 2 min |  |
| Measurement time, no more than | 2 sec |  |
| Alarm indication | Visual and audible alarms when thresholds are exceeded. Haptic alarm is an advantage. |  |
| Power supply | From integrated rechargeable battery |  |
| Time of continuous operation at gamma background (not more than 0.5μSv/h) under non-alarm conditions, no less than | 8 hours |  |
| Weight | Smaller weight of components (less than 0.7 kg) is an advantage. |  |
| Physical dimensions | Compact, portable, suitable for handheld use. Comfortable carrying handle and attachment to clothing is an advantage. |  |
| Shockproof | Yes |  |
| Waterproof | Protection grade of main components: IP 5X or better - for gamma radiation detectors, IP 2X or better - for alpha and beta radiation detectors. |  |
| Mean time between failures, no less than | 4000 hours |  |
| Service life, no less than | 6 years |  |
| ENVIRONMENTAL REQUIREMENTS |
| Ambient temperatures | From -20 to+45 0C |  |
| Relative humidity | Up to 95% at ambient temperature of 350C and lower, without condensation of moisture |  |
| PRESERVATION AND PACKAGING |
| Packaging | Protection for transportation, handling and reliable storage without re-preservation within 1 year upon delivery. |  |
| OTHER REQUIREMENTS |
| Certified for use in Ukraine | Yes |  |
| Visibility of Norwegian financing | Any equipment delivered under the contract should be clearly identified and should have metallic plates or indelible labels containing the flag of Norway and the phrase “Provided with support from the Government of Norway” in Ukrainian and in English. |  |

# DOCUMENTATION

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DOCUMENTATION |
| Technical specifications | In Ukrainian/Russian |  |
| Operator’s manual | In Ukrainian/Russian |  |
| Passports for technical means | In Ukrainian/Russian |  |
| Certificate of primary metrological verification | In Ukrainian/Russian |  |
| Certificates or documents attesting to certification of the measurement instrument in Ukraine | In Ukrainian/Russian |  |
| Training documentation | In Ukrainian/Russian |  |
| Transportation documentation | In English and Ukrainian |  |

# DELIVERY TERMS AND CONDITIONS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DELIVERY TERMS AND CONDITIONS |
| Terms of Delivery | DDP, Incoterms 2010 |  |
| Place of Delivery | 125 S. Paradzhanova St., 10025, Zhytomyr, Ukraine |  |
| Delivery Time | ≤ 120 calendar days after the date of contract signature |  |

# TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Place of training (training room to be provided by the Recipient) | Zhytomyrskiy Border Detachment of SBGS: 55A T. Shevchenko St., Ovruch City, 11101, Zhytomyr region, Ukraine |  |
| Duration of training course | 2 days |  |
| Language of training course | Ukrainian or English |  |
| Number of trainees, up to | 50 persons |  |
| Themes to be covered | - Nature of ionizing radiation, - Interaction of ionizing radiation with matter, - Radioactive sources and nuclear materials to be detected using the survey meter, - Operating principles of measuring instruments, - Detailed analysis of algorithms and features of operation, - Use of measuring instrument, - Setting-up procedures, - Procedures of calibration and measurements, - Maintenance, - Minor repairs. |  |
| Theoretical part duration, no less than | 1 day |  |
| Practical part duration, no less than | 1 day: practical training at Recipient’s training room and/or at border check point |  |
| Instructional video | Optional |  |
| Verification | Test, written form |  |
| TRAINING COURSE DOCUMENTATION |
| One certificate per trainee | In Ukrainian and English |  |
| List of materials to provide per trainee | - Set of training materials; - User’s documentation; - Training materials on one CD/DVD. |  |
| Training materials language | In Ukrainian/Russian |  |
| Results of test after training should be delivered to the Contracting Authority and Recipient | Yes |  |

# WARRANTY AND POST-WARRANTY SERVICES

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| WARRANTY AND POST-WARRANTY SERVICES |
| Duration of warranty period | ( 24 months |  |
| Place of warranty repairs and maintenance | Ukraine |  |
| Presence of official representative of the manufacturer or authorised service centre in Ukraine | Yes |  |
| Technical support during warranty and post-warranty period | Technical support by email or telephone in Ukrainian/English to solve any technical problems (software failure, anomalous behaviour, minor improvements concerning process, functional capabilities of data processing, etc.) and rectify any system-disabled state |  |
| After-sales service | Compulsory after-sales service to be provided under a separate agreement with the Recipient shall include the following: - Maintenance and post warranty repair of the Equipment on the territory of Ukraine; - Rapid provision of spare parts and consumables. |  |

# TIME SCHEDULE

| No. | Action | Period of completion | Tenderer’s Offer |
| --- | --- | --- | --- |
| 1. | Submission of documents: Technical specifications. | Within 45 calendar days after the signing of Contract |  |
| 2. | Submission of documents: Operator’s manual, Passports/logbooks for technical means, Certificate of primary metrological verification, Certificates or equivalent documents attesting to certification of the measurement instrument in Ukraine, Transportation documentation. | 2 weeks before the scheduled shipment and supplied with equipment |  |
| 3. | Submission of documents: Training course documentation. | 2 weeks before the scheduled training |  |
| 4. | Equipment delivery | Within 90 calendar days after the signing of Contract |  |
| 5. | Training of personnel | Within 90* calendar days after the signing of Contract |  |

Note: *) The personnel training must be carried out not later than within ninety (90) calendar days after the signing of Contract. The actual dates of training shall be confirmed by the Recipient and Contracting Authority no later than ten (10) days before the training course.

Authorized person on behalf of the Tenderer:

Name: ____________________________________________

Title: ______________________________________________

Signature: ________________________________________

Date: ______________________________________________